## Slide 1
DES Project
Team 3

## Slide 2
CONTENTS
CAN
Circuit Diagram
01
02
03
04
Rpi Processes
GUI Application
05
Structure
DES
INSTRUMENT
CLUSTER

## Slide 3
Structure
ECU
Processor
D bus

## Slide 4
Role of each pin
Circuit Diagram
5V
The 5V voltage is used to power and operate within electronics.
It is used to receive and send input and output signals of sensors.
GND serves as the electrical reference point in electronic devices.
GND
D1
AO
DO
GND
VCC
CAN High
CAN Low
Arduino Nano
Ultrasonic Sensor
RPM Sensor
CAN Module

## Slide 5
Preparation for CAN communication with Arduino is finish!
Arduino CAN connection
Arduino ide and basic configuration must be completed.
Step 01
How to connect CAN?
Install CAN Library
We choose autowp-mcp2515
Step 02
Set Bitrate
Every ECU have to set same bitrate
Step 03
Set Frequency
The frequency is set according to the shield
Step 04
Connect with CAN shield
Connect the correct pin number and CAN H, L

## Slide 6
If the connection is complete, check it with candump
RPi CAN connection
RPi OS and basic configuration must be completed.
Step 01
How to connect CAN?
Enable I2C interface
Choose Interfacing Options -> I2C -> Yes.
Step 02
Install libraries
Install BCM2835, Wiring Pi, python-can
Step 03
modify config.txt
The process of setting the pin number of RPi
Step 04
Set bitrate and Frequency
Same way as arduino

## Slide 7
CAN Data Sent from Arduino
The two sensor data are stored and transmitted in CAN Data field respectively.
Ultrasonic sensor
Send distance data
Stored in bytes CAN Data Field so [0] [1]
What data is sent by CAN?
In Raspberry Pi
This data is received from Arduino
RPM sensor
Send RPM data
CAN Data Field
Stored in bytes CAN Data Field so [2] [3]

## Slide 8
Distance : data[0] + data[1]*256
CAN Data Frame
Distance % 256 | Distance / 256 | RPM % 256 | RPM / 256 | 0 | 0 | 0 | 0
RPM : data[2] + data[3]*256
Data exceeding 8 bits can be transformed in this way.

## Slide 9
How to transfer battery voltage to battery level?
We perform regression analysis on each set of data to estimate the values using a sin function
Battery Indicator
Battery Level = 0.498 * sin(1.546*Voltage + 1.001) + 0.48
Regression

## Slide 10
Processes
Dashboard
CAN Receiver
PiRacer Controller
Session Bus
Responsibilities
Fetch data that needs to be displayed
Display it to user in GUI
Fetch RPM, distance data from CAN Bus
Provide interface and methods to DBus
Control and monitor PiRacer vehicle
Provide interface and methods to DBus

## Slide 11
Blocking Problem
Method call must wait until current task is done
Thread can only handle
1 task at a time

## Slide 12
Using Multi Thread
Main thread can return
latest value immediately on request
Updating thread will update values periodically without blocking the main thread

## Slide 13
CAN-Receiver

## Slide 14
PiRacer

## Slide 15
Adding Robustness
Auto starts at boot time
Parent process monitors children and can auto restart on child’s failure

## Slide 16
QT GUI Application
Distance
Output rear Distance Data
Output Battery Level
Battery level
Speed
RPM
Features
Output Current Speed
Output Current RPM

## Slide 17
Flutter GUI Application
Battery level is represented on
top right side of the screen
Battery
Speed is indicated by
running speed of Nyan Cat
Speed
Not Qt,
but Cutie
Cute
Features

## Slide 18
Live Demo

## Slide 19
Conclusion
We have deep dived into both software and hardware
We have created responsive dashboard application by using multi threaded server
We have designed a software architecture that is easy to maintain and robust

## Slide 20
Q&A

## Slide 21
Thank you